## Slide 1: Q&A Response Absorber Component modeling
Colby Magee

## Slide 2
Why do you need to develop models for absorber? What models already exist and why they do not meet your requirements.
One of the things I was wondering about was gains regarding the use of a physics-based transient model. It is easy to guess that there would be some inaccuracies when using a polynomial or stead-state model. Did anything in particular or your work make you run into limitations regarding the current models?
What is an absorption cycle? What is the curve model in Dymola?
What is the Kalina cycle? You mention it briefly in the start of the presentation and mention how it is similar to the Rankine cycle which some key differences, but what additional information can you give about the Kalina cycle?
When you compare the new physics-based absorber with the existing EES model and your Modelica implementation, which output variables define the 10% difference - capacity, outlet temperatures, or solution concentration? And does the same 10% band apply to the transient case, where the error varies over the trajectory?
What are the fundamental mass and energy balance equations needed to start building this specific Ammonia-Water absorber component model?
What chemical interactions are the most important to capture in the absorber model?
How do you plan to validate your model to determine whether it captures the physics well or not?
Which outputs will you use to check the 10% agreement target?
Direct Questions
Why new absorber model
Kalina Cycle
Criteria for comparison
What is absorption Cycle
Important Chemical Kinetics
Lumped Questions

## Slide 3
What is an absorption Cycle
Replaces the compressor in VCC with generator and absorber
In the absorber water absorbs ammonia and releases heat
In the generator heat is applies and separates the solution into water and high-pressure ammonia
Ammonia then continues to coils& expansion valve as in VCC
Pumps liquid so electricity cost is << than VCC
Technically only requires a Heat flux to cool
Use the natural attraction of ammonia and water to create high pressure high temperature ammonia vaper.

## Slide 4
What Is a Kalina Cycle
Variation of Rankine
Can be 10% - 20% more efficient than baseline Rankine
Uses Water ammonia as working fluid
Area of research for combined cooling & power plants
Learn Engineering, 2013, "Kalina Cycle Power Plant," YouTube video, accessed September 10, 2026, https://www.youtube.com/watch?v=28ckvW7FJsM

## Slide 5
Why New absorber Model
There are two existing model easily attainable
Dymola Building library Curve fit
Curve Fit model solves for needed heat addition and uses water temperature as input
This is the opposite of how a CCP model would work (waste heat from Kalina cycle  powers absorption)
Difficult to integrate into CCP
( In addition to interoperation inaccuracies of curve fit)
EES Steady state
EES model is incapable of performing transient modeling
Both Models are incapable of modeling effects of variable heat flux
Eventually I would like to answer the question: How does concentrated solar contend as a heat source for absorption cycles

## Slide 6
Chemical Kinetics
Currently identified Equation from literature
The water absorbing ammonia is the most important interaction in the absorber
Absorption Rate
Water absorption capacity
Flow Rate Out

## Slide 7
Criteria for Comparison
Simplest Model
Ammonia | Water ( week Solution) | Absorber
Mass Flow Rate | Mass Flow Rate | Absorption rate
Temperature | Temperature | Operating pressure
Pressure | Pressure | 
 | Quality | 
Knowns (model Input)
Heat Release
Output to compare
Ammonia | Absorber
Mass Flow Rate | Absorption rate
Temperature | Operating pressure
Pressure | Heat Flux in
Final Model
Output to compare
Water | Absorber
Temperature | Heat release
Mass Flow Rate | Strong solution mass flow
Quality | 
Knowns (model Input)